## Slide 1
IDS - ICMS
Use Case Pitch
18 November 2020

## Slide 2
Why?
Linking International Construction Measurement Standards (ICMS) to ifc
ICMS is a high-level reporting standard for buildings and infrastructure
Developed by RICS and other international bodies as a coalition
buildingSMART now a member
Designed to provide consistent benchmarking information on an international basis
Architecture supports cost reporting across ‘ACROME’:
  Acquisition, Construction, Renewal, Operations, Maintenance and End-of-life
To support cost benchmarking ICMS needs summary asset, site, contract and cost data for like-for-like comparisons
ifc can provide part of the ICMS dataset with other data sources completing the full picture
Next version of ICMS will address embodied carbon and carbon usage through construction and operational phases
An ICMS data standard has already been developed in xsd and json

## Slide 3
What & How?
Linking International Construction Measurement Standards (ICMS) to ifc
Author not a subject matter expert on ifc…
But has led the development of the ICMS Data Standard
Initial mapping of ICMS to ifc has identified subset of shared objects
Observations:
  ICMS asset attributes are high-level e.g. overall dimensions, floor plate areas based on finished surfaces, shell etc.
  Cost data usually held outside ifc but could be stored in ifc cost objects
  Additional data/property sets around ifc objects such as ifcSite and ifcProject could enhance ICMS support
ICMS Data Standard already aligned with ifc through use of ‘common’ objects:
  Building
  Storey/Floor
  Space
  Zone
  Site
  Project

## Slide 4
What information is needed?
Linking International Construction Measurement Standards (ICMS) to ifc
Project information on client, contract type, procurement etc.
Site information on location, conditions, use, legal status etc.
Asset information on dimensions, functional capacity, nature and complexity of works etc.
Numerical, dimensional, information might be better suited to a separate API to aggregate detailed geometric items from ifc?